## Slide 1: Design of Digital Circuits Lab 1 Supplement: Drawing Basic Circuits
Prof. Onur Mutlu
ETH Zurich
Spring 2020
28 February 2020

## Slide 2: What We Will Learn?
In Lab 1, you will design simple combinatorial circuits
We will cover a tutorial about:
  Boolean Equations
    Logic operations with binary numbers
  Logic Gates
    Basic blocks that are interconnected to form larger units that are needed to construct a computer

## Slide 3: Boolean Equations and Logic Gates

## Slide 4: Simple Equations: NOT / AND / OR
A
B
A · B
A • B (reads “A and B”) is 1 iff A and B are both 1
A
B
A + B
A + B (reads “A or B”) is 1 iff either A or B is 1
A
(reads “not A”) is 1 iff A is 0
0 | 1
1 | 0
0 | 1
1 | 0
 |  | •
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 5: Boolean Algebra: Big Picture
An algebra on 1’s and 0’s
  with AND, OR, NOT operations
What you start with
  Axioms: basic stuff about objects and operations you just assume to be true at the start
What you derive first
  Laws and theorems: allow you to manipulate Boolean expressions
  …also allow us to do some simplification on Boolean expressions
What you derive later
  More “sophisticated” properties useful for manipulating digital designs represented in the form of Boolean equations

## Slide 6: Common Logic Gates

## Slide 7: Boolean Algebra: Axioms
1. B contains at least two elements,
0 and 1, such that 0 ≠ 1
2. Closure a,b B,
(i) a + b B
(ii) a • b B
3. Commutative Laws: a,b B,
(i) a + b = b + a
(ii) a • b = b • a
4. Identities: 0, 1 B
(i) a + 0 = a
(ii) a • 1 = a
5. Distributive Laws:
(i) a + (b • c) = (a + b) • (a + c)
(ii) a • (b + c) = a • b + a • c
6. Complement:
(i) a + a' = 1
(ii) a • a' = 0
English version
Result of AND, OR stays
in set you start with
For primitive AND, OR of
2 inputs, order doesn’t matter
There are identity elements
for AND, OR, give you back
what you started with
• distributes over +, just like algebra
…but + distributes over •, also (!!)
There is a complement element,
ANDing, ORing give you an identity
Formal version
Math formality...

## Slide 8: Boolean Algebra: Duality
Interesting observation
  All the axioms come in “dual” form
  Anything true for an expression also true for its dual
  So any derivation you could make that is true, can be flipped into dual form, and it stays true
Duality -- More formally
  A dual of a Boolean expression is derived by replacing
    Every AND operation with... an OR operation
    Every OR operation with... an AND
    Every constant 1 with... a constant 0
    Every constant 0 with... a constant 1
    But don’t change any of the literals or play with the complements!
➙ a + (b • c) = (a + b) • (a + c)
a • (b + c) = (a • b) + (a • c)
Example

## Slide 9: Boolean Algebra: Useful Laws
Operations with 0 and 1:
Idempotent Law:
Involution Law:
Laws of Complementarity:
Commutative Law:
1. X + 0 = X
2. X + 1 = 1
3. X + X = X
4. = X
5. X + = 1
6. X + Y = Y + X
AND, OR with identities
gives you back the original
variable or the identity
AND, OR with self = self
double complement =
no complement
AND, OR with complement
gives you an identity
Just an axiom…
1D. X • 1 = X
2D. X • 0 = 0
3D. X • X = X
5D. X • = 0
6D. X • Y = Y • X
Dual

## Slide 10: Useful Laws (cont.)
Distributive Laws:
Simplification Theorems:
9. X • Y + X • = X
10. X + X • Y = X
11. (X + ) • Y = X • Y
9D. (X + Y) • (X + ) = X
10D. X • (X + Y) = X
11D. (X • ) + Y = X + Y
8. X • (Y+ Z) = (X • Y) + (X • Z)
8D. X + (Y• Z) = (X + Y) • (X + Z)
Associative Laws:
7. (X + Y) + Z = X + (Y + Z)
= X + Y + Z
7D. (X • Y) • Z = X • (Y • Z)
= X • Y • Z
Parenthesis order
doesn’t matter
Axiom
Useful for
simplifying
expressions
Actually worth remembering — they show up a lot in real designs…

## Slide 11: DeMorgan’s Law
Think of this as a transformation
  Let’s say we have:
  F = A + B + C
  Applying DeMorgan’s Law (12), gives us:
DeMorgan's Law:
12.
12D.

## Slide 12: DeMorgan’s Law (cont.)
X | Y |  |  |  | 
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0
X | Y |  |  |  | 
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
NOR is equivalent to AND
with inputs complemented
NAND is equivalent to OR
with inputs complemented
X
Y
X
Y
A
A
X
Y
X
Y
B
B
Interesting — these are conversions between different types of logic
That’s useful given you don’t always have every type of gate

## Slide 13: Part 1: A Comparator Circuit
  Design a comparator that receives two 4-bit numbers A and B, and sets the output bit EQ to logic-1 if A and B are equal
  Hints:
    First compare A and B bit by bit
    Then combine the results of the previous steps to set EQ to logic-1 if all A and B are equal
Comparator 1
A
B
EQ (A=B)
4 bits
4 bits

## Slide 14: Part 2: A More General Comparator
Design a circuit that receives two 1-bit inputs A and B, and:
  sets its first output (O1) to 1 if A>B,
  sets the second output (O2) to 1 if A=B,
  sets the third output (O3) to 1 if A<B.
Comparator 2
A
B
O1 (A>B)
O2 (A=B)
O3 (A<B)

## Slide 15: Part 3: Circuits with Only NAND Gates
Design the circuit of Part 2 using only NAND gates
Logical Completeness:
  The set of gates {AND, OR, NOT} is logically complete because we can build a circuit to carry out the specification of any combinatorial logic we wish, without any other kind of gate
  NAND and NOR are also logically complete

## Slide 16: Last Words
In this lab, you will draw the schematics of some simple operations
Part 1: A comparator circuit
Part 2: A more general comparator circuit
Part 3: Designing circuits using only NAND gates
You will find more exercises in the lab report

## Slide 17: Report Deadline
23:59, 20 March 2020

## Slide 18: Design of Digital Circuits Lab 1 Supplement: Drawing Basic Circuits
Prof. Onur Mutlu
ETH Zurich
Spring 2020
28 February 2020